## Slide 1: IMU sensor fusion and orientation estimation
Lab: B4, HI1033

## Slide 2: Components of an IMU
Accelerometer measures linear acceleration and is affected by gravity
Gyroscope measures angular velocity
Magnetometer measures earth's magnetic field
Applications: smartphones, drones, vr systems, navigation systems, motion tracking

## Slide 3: Why sensor fusion?
Imu sensors provide motion data but, raw measurements cointains errors:
Accelerometer is sensitive to noise and dynamic motion
Gyroscope is accurate short-term but drifts over time
Magnetometer is affected by magnetic interference

## Slide 4: Orientation angles
Pitch: rotation around the X-axis (forward-bakward tilt)
Roll Rotation around the Y-axix (sideways tilt)
Yaw: rotation around the z-axis (rotation around the vertical axis
x
x
y
y
z
z

## Slide 5: Method 1: Accelerometer + EWMA
Uses gravity for orientation estimation
Can estimate picth and roll
Sensitive to dynamic acceleration
Cannot estimate yaw
Sensitive to motion noise

## Slide 6: Method 2: complementary filter
Combines:
Accelerometer: long-term stability
Gyroskop: fast response
Advantages: smoother orientation estimation, better motion responsiveness
Limitations: gyroscope drift over time, yaw instability during long-term rotation

## Slide 7: Method 3: Madgwick algoritm
Combines: accelerometer, gyroskop and magnetometer data
Estimates pitch, roll and yaw simultaneously
Features: quaternion-based orientation, real-time sensor fusion and stable yaw estimation
Fill 3d orientation
qt = updated quaternion orientation
q˙\dot{q}q˙ = gyroscope-based quaternion derivative
Δt\Delta tΔt = sampling interval
β\betaβ = correction factor
∇f(q)\nabla f(q)∇f(q) = gradient descent correction
Advantages: Full 3D orientation estimation, Reduced yaw drift, Low computational cost, Suitable for mobile systems
Limitations: Sensitive to magnetic interference, Requires magnetometer calibration, Yaw can become unstable in noisy environments

## Slide 8: Comparison
Method | Sensors | Pitch | Roll | Yaw
EWMA | Acc | Yes | Yes | No
Complementary | Acc + Gyro | Yes | Yes | Partial
Madgwick | Acc + Gyro + Mag | Yes | Yes | Yes

## Slide 9: Implementation Across mobile plattforms
Plattform | Sensor Framework | Notes
Android | SensorManager | Direct access to accelerometer, gyroscope and magnetometer
iOS | Core Motion | Built-in motion tracking and sensor fusion
React Native (Cross-plattform) | Expo Sensors / Native Modules | Cross-plattform developement for Android and iOS

## Slide 10: Android implementation
The center of the screen represents the origin position of the visualization.
Inner white marker representing yaw direction

## Slide 11: Godot (Open source 2d and 3d game engine)
Visualize orientation in a 3d enviroment

## Slide 12: Godot Implementation
Godot orientation match game
The goal is to match blue cube’s orientation to green cube using device’s orientation data
The system caculates error values and shows matches within

## Slide 13: Upcoming laboratory exercise: Lab b.4
Real-time visualisation
Comparasion between orientation estimation methods

## Slide 14: Resources
Godot Engine: https://godotengine.org/
Android implementation: https://github.com/Hadiseh04/Madgwick
Lab B.4 Instructions: Madgwick/Lab B.4.pdf at main · Hadiseh04/Madgwick